## Slide 1: Implementación en FPGA de una arquitectura para la reconstrucción acelerada de imágenes de pMRI a partir de datos de k-espacio
Weekly report: 27/02/2026
Font Julian

## Slide 2: Phased array coils
Week: 20/02/2026

## Slide 3
Continuos Time
Mathematical description of aquisition domains

## Slide 4
Discrete Time
Mathematical description of aquisition domains

## Slide 5
Sensitivity map: pre-scan method

## Slide 6: Raw data from coils k-space
SENSE algorithm input
If no undersampling applied: Af = 1

## Slide 7
SENSE with Af = 1: pixel by pixel model
Let’s take one pixel, e.g. (1,1)
Vector notation:
(noise is ignored for simplicity)

## Slide 8
SENSE with Af = 1: least-squares solution
We need to find the value of m that minimizes the quadratic error between the data and the model
Data
Model
This is an optimization problem, written as:

## Slide 9
SENSE with Af = 1: Moore-Penrose pesudoinverse
This is a well-known problem and can be resolved using the Moore-Penrose pseudoinverse, written as:
Decomposed as:

## Slide 10: Raw data from coils k-space
SENSE algorithm input
Undersampling applied: Af = 2
Undersampling in (acceleration factor causes pixels of the full-FOV image to fold into one aliased pixel in each coil image.
Images are displayed zero-filled to full for better visualization

## Slide 11
Same sensitvity maps…

## Slide 12
SENSE with Af > 1: now we gotta scale with aliasing
Let’s take one folded pixel, e.g. (, ) (Will asume undersampling in the y direction)
Matrix notation:
(again, noise is ignored for simplicity)
In example, for :

## Slide 13
SENSE with Af > 1: now we use matrices instead of vectors
With Af = 1:
With Af > 1:

## Slide 14
SENSE with Af > 1: least-squares solution
We want to estimate the vector that best explains the measured data . This leads again to a least-squares problem
Data
Model
Again, this leads to:
Note that now:
This means we can use Cholesky, LU decomposition, gauss elimination, etc

## Slide 15
Why can’t we simply compute
A simpler solution to the problem could be .
We cannot do that because we have the noise term (wich we decided to ignore).
Also, the matrix is not invertible in the classic sense because:
In practice , so is a rectangular matrix, and thus doesnt have classic inverse
What has instead, is a Moore-Penrose pseudo-inverse
Week: 27/02/2026

## Slide 16
How do we obtain the clinical image from ? Part 1
Firstly, we’re going to call the clinical data (not the image yet) as
We initialize that matrix with zeros
Then, we solve the pseudo-inverse for each aliased pixel , obtaining
Note that:

## Slide 17
How do we obtain the clinical image from ? Part 2
Now, we’re going to calculate the “real” positions of :
Then we write into the output data M
This means we are distributing the components of the vector in the rows that were folded.
After finishing this sweep we obtain

## Slide 18
How do we obtain the clinical image from ? Part 3
Now, we simply compute the magnitude of
With being the desired clinical image
=

## Slide 19
Let’s decompose the pseudo-inverse problem…
We said we have the following problem:
We can define new variables and rewrite the problem in the standard linear system form:

## Slide 20
As we defined earlier…

## Slide 21
So the matrix A should be…
Remember that
with
This is the first matrix we must compute on the FPGA as part of the SENSE reconstruction

## Slide 22
As we defined earlier…

## Slide 23
So the matrix b should be…
Again, remember that
and
This is the second matrix we must compute on the FPGA as part of the SENSE reconstruction

## Slide 24
Choosing the optimal method for solving
First, we list a couple of characteristics:
is a Hermitian positive definite matrix (HPD), which means it’s a square matrix of complex elements with the characteristics of being the same complex transpose:
We have a small system:
We have only one columna vector per system (right-hand-side)
We will normalize S and y so that we can represent them using complex fixed-point with only 1 integer bit

## Slide 25
Gauss elimination…
Consisting in applying forward elimination over , followed by backwards sustitution directly over the system
For it’s pretty cheap in absolute terms
We do not exploit the HPD structure !!
Without pivoting it could be pretty unstable in fixed point operations
With partial pivoting we got better stability, but with the complex hardware logic trade-off
The complexity of the algorithm is FLOPs for the elimination pase and for the two triangular substitutions

## Slide 26
LU decomposition…
Consisting in factorizing , with the lower triangular matrix and the upper triangular matrix
The complexity of the algorithm is for FLOPs and for sustitutions (same as GE)
Again, we do not exploit the HPD structure !!

## Slide 27
Cholesky…
In Cholesky decomposition, we have that for Hermitian positive matrices:
The complexity of the algorithm is for FLOPs and for sustitutions (half of GE and LU)C
For Hermitian positive matrixes, Cholesky is very stable even with fixed point arithmetic. But we gotta be carefoul in rounding that A is always Hermitian positive
We do not need pivoting; HPD guarantees positive diagonal elements during factorization
We only needs to store half of the A matrix; upper or lower triangular
Hermitian symmetry allows us to reuse many terms

## Slide 28
Let’s go back to the pixel-wise operations…
Before computing the solution to the matrix system, we’re going to find the A and b matrixes in the FPGA as follows
Again, remember that
and

## Slide 29
Let’s go back to the pixel-wise operations…
Let’s do an example:
We can exploit the Hermitian symmetry of A as follows
The good news is that we only need to compute ,

## Slide 30
Let’s go back to the pixel-wise operations…
Let’s do an example:

## Slide 31
Complex multiply-accumulate operations for A and b

## Slide 32
Let’s start some floating point simulations. Part 1 …
First, we’re going to generate a target, following a phantom called “Shepp Logan” of size N x N = 32 x 32
Mag
Phase

## Slide 33
Let’s start some floating point simulations. Part 2 …
Now, we’re going to generate synthetic sensitivity maps, assuming L = 4

## Slide 34
Let’s start some floating point simulations. Part 3 …
With the sensitivity maps generated, now we do the pixel-wise multiplication between the phantom and the maps

## Slide 35
Let’s start some floating point simulations. Part 4 …
Now we obtain the k-space from the coil images with the sensitivity maps applied

## Slide 36
Let’s start some floating point simulations. Part 5 …
Now we apply aliasing in the k-space in the direction with an undersampling factor of

## Slide 37
Let’s start some floating point simulations. Part 6 …
We can apply the Inverse Fourier Transform to get the aliased images in the image space

## Slide 38
To be continued …